## Slide 1: From Material Passports to Digital Product Passports Creating and Validating Linked Data-based Digital Product Passports for the AEC industry
Janneke Bosma, 1733133 MAY 2024
Master Construction Management & Engineering

## Slide 2: Problem statement
Not all materials infinite
Processing and utilization results in significant CO2 emissions.
The construction sector contributes to 38% of total global energy-related CO2 emissions.
  Material Passports can be a solution. However, there is no standard and no consensus among stakeholders regarding the content of the passport.
  There is a need to verify the data to ensure its accuracy, thereby enhancing the prospects for reusing and recycling materials.
Refuse
Reduce
Renew
…Recycle
10R
  Minimize by acting higher on the 10R ladder. However, there are several challenges involved to renew (reuse) materials.
MP
Notes:   Not all materials possess infinite utility. Moreover, the processing and utilization of these materials result in significant CO2 emissions.
  The construction sector contributes to 38% of total global energy-related CO2 emissions.
  To minimalize this there is need for ‘refuse’, ‘reduce’, and ‘renew’ even above recycling. However, there are several challenges involved to renew (reuse) materials.
  Material Passports can be a solution to the challenges, such as connecting supply and demand. However, there is no standard and no consensus among stakeholders regarding the content of the passport.
  Furthermore, there is a need to verify the data to ensure its accuracy, thereby enhancing the prospects for reusing and recycling materials.

## Slide 3: Agenda
Literature Material Passports & Digital Product Passports
Research Questions
Conclusion
The process (DPP format and validation process)
Evaluation
Discussion
Contribution & recommendations

## Slide 4: Material Passport
MP
Optimization tool & variant studies
Exact material composition
Second-hand raw material register
Material,
product &
component
Sustainable and circular characteristics, value, and opportunities
Single identifiable product and associated life cycle information
Digital interface
Function MP
Definition MP
No standard
format
BAMB
CB’23
Madaster
Nutrition certificates
BIM data
Eco-labels
Cradle-to-cradle passport
Digital Building Logbook
Notes: Digital interface;
Single identifiable product and associated life cycle information ;
Gaining insight into sustainable and circular characteristics, value, and opportunities;
Not only of the product, but also underlying components and materials.
Mpa - serves as a rough estimation and optimization tool. Variants studies can look at the most appropriate construction based on recycling potential and environmental impact. This phase has the most impact in terms of recycling, waste and environmental impact. When using BIM, it is important here that the geometry is properly modulated and the elements are assigned the correct classification.
MPb - also functions as an optimization tool. Here e.g. thicknesses and layers of the applied product/material can still be adjusted.
MPc - During the tender phase, the exact material composition can be checked.
MPd- Serves as documentation in which the final situation is recorded and this can serve as a second-hand raw materials register.
A lot of existing passports and alternatives however scope and definition differ. No standard. Movement from Europe to a dpp

## Slide 5: Challenges
Unclear exactly what belongs in a passport (no format);
The purpose of the passport differs, creating confusion among stakeholders about the benefits of a passport;
The above also creates limitations in creating (semantic and technical) standards to implement;
Etc..
(Adams, 2008)
Figure 1: Managing expectations

## Slide 6: From material passport to digital product passport
DPP
Manufacturing data
Usage data
Life cycle data
Expected to become ‘mandatory’ in 2026
Track and trace tool
Seen as a solution to the lack of consistent and trustworthy information
Literature terminology DPP & MP used interchangeably
No standard
format
Subject to various regulations and standards, some of which are only now emerging
End-of-life data
Type of data
State-of-the-art
Notes: In the literature, the terminology of an MP and DPP is used interchangeably;
DPP is seen as a solution to the lack of consistent and trustworthy information;
It can serve as a track and trace tool;
Expected to become ‘Mandatory’ in 2026.
The DPP is subject to various regulations and standards, some of which are only now emerging
Manufacturing data, usage data, end-of-life data & life cycle data

## Slide 7: Digital product passport
The stakeholder (economic operator) who places the object on the market is responsible for creating the DPP and making it available to the public.
A lot of information will need to be exchanged during the life cycle of the object.
Linked data can form a solution to prevent data loss.
Linked Data is a way to organize and connect information on the internet so that computers and people can easily communicate and understand each other.
Figure 2: Cumulative DPP addition through the object life cycle

## Slide 8: Differences DPP and MP
DPP
MP
Pre-conceptual phase
Demonstration phase
Any physical good placed on the market or put into service
Composition, origin, repair, and dismantling information. Handling information at the end of its service life
Repair, production, and disposal to complete life-cycle
Suppliers, manufacturers
Consumers, market surveillance. Any industry
Building materials
Information on reuse of materials; cross-ref. to data sheets, EPDs
End-of-life
The MP platform, BIM discussed
Unknown
Architects, builders, etc. Built environment
Manufacturers
Notes: In the literature, the terminology of an MP and DPP is used interchangeably;
DPP is seen as a solution to the lack of consistent and trustworthy information;
It can serve as a track and trace tool;
Expected to become ‘Mandatory’ in 2026.
The DPP is subject to various regulations and standards, some of which are only now emerging
Manufacturing data, usage data, end-of-life data & life cycle data

## Slide 9: Challenges
Existing MPs and DPPs are compared based on requirements from the literature and the later discussed must-haves. No passport is suitable at the moment.
Integrated into the existing regime and information requirements;
Varying information needs stakeholders;
Information shared through different portals and methods. Need to be consolidated in the DPP;
Absence of clear specifications leads to divergent industry-driven visions;
Obtaining product information and maintaining the DPP’s accuracy;
Currently no format available;
Etc.

## Slide 10: Research question
How can a Digital Product Passport for the AEC industry be created and validated using BIM and semantic technologies?
This main question will be split up into multiple sub-questions. These include:
What is the current state-of-the-art of MPs, DPPs, automated data validation tools, BIM-based technologies, and semantic technologies?
Which parts of a DPP will need to be validated and which part of the validation process is required by the contractor?
How can a proof-of-concept for the DPP validation method be developed and tested in a real-world use case?
How can the validation process and output be visualized and feedback - provided to the end user?

## Slide 11: Conclusion
  How can a digital product passport for the AEC industry be created and validated by the use of BIM-based and semantic technologies?
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Define must-haves
DPP
Define requirements
Convert IFC to linked data
DPP ontology
Enrich /improve data & create material & product database
Set validation rules
SHACL
PySHACL
IFCtoLBD
Perform validation
Validation report
Collect data
(IFC)
Notes:     DPP must-haves are defined;
    Requirements are defined (not discussed today);
    IFC models converted to Linked data;
    A DPP Ontology is proposed;
    The data is enriched, and a material and product database is made;
    Validation rules are established and written in SHACL;
    The PySHACL script is adapted and used to perform the validation;
    A validation report is generated and the IFC GUID can be used to improve the source documentation
    All these steps constitute the validation process

## Slide 12: The process
Material Passport and Digital Product Passport
Requirement definition
Data collection
Ontology creation
Data preparation
Validation rules and rule preparation
Rule execution
Validation report
Mock- up & Prototype evaluation
Discussion, Conclusion, Recommen-dations & Contribution
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 13: The process
Material Passport and Digital Product Passport
Requirement definition
Data collection
Ontology creation
Data preparation
Validation rules and rule preparation
Rule execution
Validation report
Mock- up & Prototype evaluation
Discussion, Conclusion, Recommen-dations & Contribution
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 14: Define topics DPP (must-have)
Geometric data | Circularity | Material circularity characteristics | General product information | Other
Dimensions | Recycling potential | Material composition | Product name/details | Building location
Weight | Reusability potential | Material criticality | Product object number | Updates
Density | Disassembly potential | Secondary material | Manufacturer article nr. | Time
Geometry | Future function | Origin | Temporal info | Condition assessment
Quantity | Circularity |  | Location in building | 
 |  |  | Warranties | 
 |  |  | Disassembly instructions | 
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Table 1: Defined must-have topics
Notes:   Missing topics from the workshop
  Environmental Product Declaration;
  General info (coordinates, object number, etc);
  Data on maturity (maturity measurements);
  Strategically scarce materials;
  Inspections during the construction phase;
  Information about the environment (e.g. subsoil)
  Information on weather conditions during execution.

## Slide 15: Data structures (UML)
    Must-have topics are structured in a UML-diagram;
    This to understand the various components that must be validated and their interrelationships.
    Forms a basis for the following steps in the process
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 16
Building levels
Circularity
Manufacturer
Classification code
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 3: Data structure DPP

## Slide 17: Example Class and Property
Class
Property
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 4: Example class and property

## Slide 18: Data collection
    IFC Models
    Transformation building
      2 Concrete walls
      Insulation
      Wall cladding
    Terraced house
      Door
      Window
      Concrete wall
    Both models do not contain all must-have data
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 5: IFC model tranformation building and terraced house
Notes: In the built environment IFC is used a lot. E.g. a model can be made in the program revit. To share this information it is converted to IFC so different stakeholders can work together even if they used different BIM software. As long as it all is converted to IFC.

## Slide 19: Ontology creation
    Currently, there is no ontology for DPPs and MPs available
    Based on the defined must-have topics in the UML a new ontology is proposed: the DPP ontology (focus on element, product, and material level)
    For some must-have topics existing ontologies can be reused
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Notes: Wat is een ontology visueel

## Slide 20: Ontology creation
    T box – only shows classes
    Dark green shows the usage of the DPP ontology
    The light green boxes show the alternative existing ontologies
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 6: T Box digital product passport ontology
Building levels
Circularity
Manufacturer
Classification code

## Slide 21: Ontology landscape
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 7: Ontology landscape
*
*QUDT is currently used, but OM is recommended

## Slide 22: Data preparation
IFC
Linked data
Check data
Add must-haves
Create material & product data
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Notes:     The models of the Transformation building, and Terraced house are translated to Linked data as well by using a python script
    After the models are converted:
      Some mistakes in the files are removed to make the data work
      For both buildings a new file is made which includes the missing must-have topics
      For both buildings a belonging materials and product database is created in linked data

## Slide 23: Data preparation
    Example: Product data of concrete in Linked data format.
    This is a section of the DPP
IFC
Linked data
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Fragment 1: Snippet of digital product passport product concrete

## Slide 24: Validation rules
    Next step is to validate the data (must-have topics).
    Currently, no requirements within the relevant sustainability themes of MPs or DPPs.
    Lee et al. (2016) created a rule-based validation method for the validation of IFC models.
(Lee et al, 2016)
Proposed in this thesis
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Table 2: Validation rules

## Slide 25: Rule preparation
    This validation will be done by using Shape Constraint Language (SHACL)
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Fragment 2: Snippet of SHACL reusability potential

## Slide 26: Rule execution
    To execute the rules a Python script is used
PySHACL
Report
Building, product & material data
SHACL Rules
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 27: Rule execution
PySHACL
Python
Missing classes
IFC GUID
& PDF Format
Validation report
Python
Python
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Notes: -Mention an example of a class (e.g. the product example used earlier in the presentation)

## Slide 28: The validation report
Class level
Property level
Violation: missing property service life
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 29: Dashboard Mock-up
    Next step: integrate this process in a dashboard
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 8: Mock-up dashboard part 1

## Slide 30: Dashboard Mock-up
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 9: Mock-up dashboard part 2
Figure 10: Mock-up dashboard part 3

## Slide 31: The prototype evaluation
    Process validated among employees (potential users), by using competence questions and the requirements.
    All requirements with priority 1 are met and all competence questions can be queried (all data wished to be included by potential users can be retrieved)
    Feedback:
      There need to be a manual for the process;
      There need to be an ‘owner’ for the process;
      There need to be a dashboard to enable an easier validation process;
      Etc..
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 32: Discussion
    Current converter from IFC to Linked data does not include the DPP ontology;
    Significant changes may occur for the DPP (and on what to validate) since it is a new subject, and regulations are unclear;
    Assign an owner for the validation process;
    Connection real databases and other ontologies;
    Expand DPP ontology;
    Align terminologies, e.g. material and product, based on regulations;
    Validating bigger files can be time-consuming if printed in pdf.
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 33: Contribution and recommendations
Scientific (SC) and Societal (SO) contribution
    Format dpp (SC,SO)
    Proof of concept validation process (SC)
    Current state-of-the-art MP and DPP (SC,SO)
    Use case linked data (SC)
    Extension PySHACL (SC)
    DPP ontology (SC,SO)
    Accessible linked data (SO)
  Dashboard, Incorporate feedback, Integration existing ontologies Protégé, Validate DPP throughout the entire chain, add should have topics & correctly configure BIM models and standardize data
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 34: Where to find the information?
Python scrips, SHACL file, DPP Ontology & Example files Linked data
Explanatory PowerPoints & Thesis
Example process to try it out yourself
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 35: Any questions?

## Slide 36: Bibliography
Dia 2:
Anderson, J. E., Wulfhorst, G., & Lang, W. (2015). Energy analysis of the built environment—A review and outlook. Renewable and Sustainable Energy Reviews, 44, 149–158. https://doi.org/10.1016/J.RSER.2014.12.027
Cramer, J. (2017). The Raw Materials Transition in the Amsterdam Metropolitan Area: Added Value for the Economy, Well-Being, and the Environment. Https://Doi.Org/10.1080/00139157.2017.1301167, 59(3), 14–21. https://doi.org/10.1080/00139157.2017.1301167
Mehra, S., Singh, M., Sharma, G., Kumar, S., Navishi, & Chadha, P. (2022). Impact of Construction Material on Environment. Ecological and Health Effects of Building Materials, 427–442. https://doi.org/10.1007/978-3-030-76073-1_22
Rijkswaterstaat. (2020). Materialenpaspoort.
United Nations Environment Programme. (2020). 2020 GLOBAL STATUS REPORT FOR BUILDINGS AND CONSTRUCTION Towards a zero-emissions, efficient and resilient buildings and construction sector . www.globalabc.org.
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 37: Sources
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Dia 3:
van Capelleveen, G., Vegter, D., Olthaar, M., & van Hillegersberg, J. (2023). The anatomy of a passport for the circular economy: a conceptual definition, vision and structured literature review. Resources, Conservation and Recycling Advances, 17. https://doi.org/10.1016/J.RCRADV.2023.200131
Dia 4:
van Capelleveen, G., Vegter, D., Olthaar, M., & van Hillegersberg, J. (2023). The anatomy of a passport for the circular economy: a conceptual definition, vision and structured literature review. Resources, Conservation and Recycling Advances, 17. https://doi.org/10.1016/J.RCRADV.2023.200131
Honic, M., Kovacic, I., & Rechberger, H. (2019a). Concept for a BIM-based Material Passport for buildings. IOP Conference Series: Earth and Environmental Science, 225(1). https://doi.org/10.1088/1755-1315/225/1/012073

## Slide 38: Sources
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Dia 5:
Adams, S. (2008). managing expectations comic Dilbert. https://nl.pinterest.com/pin/11188699044977708/
Honic, M., Kovacic, I., & Rechberger, H. (2019a). Concept for a BIM-based Material Passport for buildings. IOP Conference Series: Earth and Environmental Science, 225(1). https://doi.org/10.1088/1755-1315/225/1/012073
Hoosain, M. S., Paul, B. S., Raza, S. M., & Ramakrishna, S. (2020). Material Passports and Circular Economy. An Introduction to Circular Economy, 131–158. https://doi.org/10.1007/978-981-15-8510-4_8/TABLES/5
Munaro, M. R., Fischer, A. C., Azevedo, N. C., & Tavares, S. F. (2019). Proposal of a building material passport and its application feasibility to the wood frame constructive system in Brazil. IOP Conference Series: Earth and Environmental Science, 225(1). https://doi.org/10.1088/1755-1315/225/1/012018

## Slide 39: Sources
Dia 6:
Adisorn, T., Tholen, L., & Götz, T. (2021). Towards a digital product passport fit for contributing to a circular economy. Energies, 14(8). https://doi.org/10.3390/EN14082289
Guth-Orlowski, S. (2021, October 18). The digital product passport and its technical implementation | by Dr. Susanne Guth-Orlowski | Medium. https://medium.com/@susi.guth/the-digital-product-passport-and-its-technical-implementation-efdd09a4ed75
Harrison, K., & Conrad, T. (2011, August). Predicting Emerging Product Design Trend by Mining Publicly Available Customer Review Data | Request PDF. https://www.researchgate.net/publication/257919571_Predicting_Emerging_Product_Design_Trend_by_Mining_Publicly_Available_Customer_Review_Data
Plociennik, C., Pourjafarian, M., Saleh, S., Hagedorn, T., do Carmo Precci Lopes, A., Vogelgesang, M., Baehr, J., Kellerer, B., Jansen, M., Berg, H., Ruskowski, M., Schebek, L., & Ciroth, A. (2022). Requirements for a Digital Product Passport to Boost the Circular Economy. Lecture Notes in Informatics (LNI), Proceedings - Series of the Gesellschaft Fur Informatik (GI), P-326, 1485–1494. https://doi.org/10.18420/INF2022_127
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 40: Sources
Dia 6:
van Capelleveen, G., Vegter, D., Olthaar, M., & van Hillegersberg, J. (2023). The anatomy of a passport for the circular economy: a conceptual definition, vision and structured literature review. Resources, Conservation and Recycling Advances, 17. https://doi.org/10.1016/J.RCRADV.2023.200131
Lell, O., Muster, V., Thorun, C., & Gossen, M. (n.d.). Förderung des nachhaltigen Konsums durch digitale Produktinformationen: Bestandsaufnahme und Handlungsempfehlungen | Umweltbundesamt. Retrieved November 30, 2023, from https://www.umweltbundesamt.de/publikationen/foerderung-des-nachhaltigen-konsums-durch-digitale
de Römph, T. J., & Cramer, J. M. (2020). How to improve the EU legal framework in view of the circular economy. Journal of Energy & Natural Resources Law, 245–260. https://doi.org/10.1080/02646811.2020.1770961
Walden, J., Steinbrecher, A., & Marinkovic, M. (2021). Digital Product Passports as Enabler of the Circular Economy. Chemie-Ingenieur-Technik, 93(11), 1717–1727. https://doi.org/10.1002/CITE.202100121
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 41: Sources
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Dia 7:
Adisorn, T., Tholen, L., & Götz, T. (2021). Towards a digital product passport fit for contributing to a circular economy. Energies, 14(8). https://doi.org/10.3390/EN14082289
Dia 8:
Cobuilder International. (2023, November 22). Navigating new EU Regulations and digital tranformation in Construction.
Cobuilder International. (n.d.). EU approach to the Digital Product Passport of the construction industry - Digital solutions for the construction industry. Retrieved March 14, 2024, from https://cobuilder.com/en/eu-approach-to-the-digital-product-passport-of-the-construction-industry/
Watson, K., Patzer, F., & Schöppenthau, F. (2023). Achieving a Sustainable Economy with Digital Product Passports. IIC Journal of Innovation.

## Slide 42: Sources
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Dia 9:
Adisorn, T., Tholen, L., & Götz, T. (2021). Towards a digital product passport fit for contributing to a circular economy. Energies, 14(8). https://doi.org/10.3390/EN14082289
Berger, K., Schöggl, J. P., & Baumgartner, R. J. (2022). Digital battery passports to enable circular and sustainable value chains: Conceptualization and use cases. Journal of Cleaner Production, 353. https://doi.org/10.1016/J.JCLEPRO.2022.131492
Eppinger, E., Jain, A., Vimalnath, P., Gurtoo, A., Tietze, F., & Hernandez Chea, R. (2021). Sustainability transitions in manufacturing: the role of intellectual property. Current Opinion in Environmental Sustainability, 49, 118–126. https://doi.org/10.1016/J.COSUST.2021.03.018
Schützenhofer, S., Kovacic, I., & Rechberger, H. (2022). Assessment of Sustainable Use of Material Resources in the Architecture, Engineering and Construction Industry ˗ a Conceptual Framework Proposal for Austria. Journal of Sustainable Development of Energy, Water and Environment Systems, 10(4). https://doi.org/10.13044/J.SDEWES.D10.0417
European Commission. (2020b). Regulation of the European parliament and of the council - concerning batteries and waste batteries, repealing Directive 2006/66/EC and amending Regulation (Eu) no 2019/1020.

## Slide 43: Material Passport
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 11: Stages of a material passport
Notes: Mpa - serves as a rough estimation and optimization tool. Variants studies can look at the most appropriate construction based on recycling potential and environmental impact. This phase has the most impact in terms of recycling, waste and environmental impact. When using BIM, it is important here that the geometry is properly modulated and the elements are assigned the correct classification.
MPb - also functions as an optimization tool. Here e.g. thicknesses and layers of the applied product/material can still be adjusted.
MPc - During the tender phase, the exact material composition can be checked.
MPd- Serves as documentation in which the final situation is recorded and this can serve as a second-hand raw materials register.

## Slide 44: Process Digital Product Passport
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude
Figure 12: DPP process scheme
Notes: Mpa - serves as a rough estimation and optimization tool. Variants studies can look at the most appropriate construction based on recycling potential and environmental impact. This phase has the most impact in terms of recycling, waste and environmental impact. When using BIM, it is important here that the geometry is properly modulated and the elements are assigned the correct classification.
MPb - also functions as an optimization tool. Here e.g. thicknesses and layers of the applied product/material can still be adjusted.
MPc - During the tender phase, the exact material composition can be checked.
MPd- Serves as documentation in which the final situation is recorded and this can serve as a second-hand raw materials register.

## Slide 45: Requirement definition
Requirements resulting from literature and the must-haves are grouped.
    User requirements, Validation process requirements & Data requirements
    Must-have requirements are graded with priority 1
    Based on the requirements and must-haves it is also determined no existing DPP/MP format is suitable to reuse for this research
MP/DPP
Req.
Collect
Ontology
Data prep.
Rule prep.
Validate
Report
Evaluate
Conclude

## Slide 46: Requirement definition
The belonging requirement (R) | 
Must-have subject | MH
Legal obligations | L
Functional suitability | F
Security, confidentiality, and IP Protection | S
Accessibility | A
Interoperability | I
Modularity and Modifiability | MM
Availability and Time behavior | AT
Portability | P
Non-Redundancy | R
Applicability | AP
Tabel 3: The requirement topics

## Slide 47: Requirement definition
User requirements |  |  | 
The user is able to … |  | P | R
1 | Validate their IFC and DPP whether the must-haves of the object are represented correctly. | 1 | MH, F
2 | Retrieve the information of the validation together with the corresponding IFC GUID of which object is wrong or missing | 1 | MH, F
3 | Make additions and modifications in the source data. | 2 | MM
4 | Remove or adapt actors, products, or attributes as requirements evolve | 3 | MM
5 | Easily understand the validation process and its results | 1 | A, AP
6 | Access the tools needed for the validation process without costs involved | 2 | AP
7 | Perform the validation process without extra steps or research needed | 2 | AP
Tabel 4: User requirements

## Slide 48: Requirement definition
Validation proces requirements |  |  | 
The validation proces should be able to … |  | P | R
1 | Query and validate the must-haves from the IFC model and DPP and communicate the results. | 1 | MH, F, AP
2 | Comply with the following legal obligations: GDPR, the EPR, the ‘right to repair’, and the ESPR. | 3 | L, F
3 | Not impede existing chain processes, product quality, or safety. | 3 | F
4 | Provide a secure data exchange between the value chain members. | 3 | S
5 | Remain the data control with the data providers to safeguard intellectual property. | 3 | S
6 | Ensure access for assigned parties through an access control mechanism. | 3 | A
7 | Ensure participation opportunities for the parties without stable internet connections or advanced IT systems. | 3 | A
8 | Ensure permanent access to the whole life cycle data. | 3 | A
9 | Visualize the data in an understandable manner. | 2 | A
10 | Exchange validation information across different company boundaries. | 2 | I
11 | Show the information when needed. |  | AT
12 | Tranfer information between software systems to enable decentralized systems. | 3 | P
13 | Guarantee origin, integrity, verifiable, compliance, and immutability. | 3 | S
14 | Be scalable for various project sizes and environments, and its current level of use and adoption | 2 | AP
Tabel 4: Validation proces requirements

## Slide 49: Requirement definition
Data requirements |  |  | 
The data should be able to … |  | P | R
1 | Show and validate the unit of measurements of the must-haves | 1 | MH
2 | Enable interoperability within and between systems by the use of shared semantics and standardized data schemes | 2 | I, P, R
3 | Be available real time (availability and time behaviour) | 3 | AT
4 | Uniquely identified, traceable, and time stamped | 1 | P
Tabel 5: Data requirements

## Slide 50: DPP ontology
Figure 13: Classes DPP
Figure 14: Data properties DPP
Figure 14: Notation alternative ontologies